## Slide 1: Hydrographic Information Harmonisation Working Group (HIHWG)
Chairperson: Jennifer Hum-Miller (hum-miller.j@forces.gc.ca) 1-613-992-7739

## Slide 2: Introduction
The use of geographic information technology to automate the production of nautical charts has been a goal of IHO and DGIWG for over 10yrs
There have been efforts to harmonise the IHO S-57 and the DGIWG DIGEST base standards since their inception
The IHO and DGIWG committees have different goals and address different communities resulting in two separate digital standards, and thus unharmonised / incompatible electronic chart products
Notes: The use of geographic information technology to automate nautical chart production has been a goal of both the International Hydrographic Organization (IHO) and of the Digital Geospatial Information Working Group (DGIWG) for over ten years.
Since the inception of the IHO S-57 and the DGIWG DIGEST there has been an effort to harmonize these base standards.
The IHO and DGIWG committees have different goals and address different communities resulting in two separate digital products for electronic charts.
As early as 1994 both committees harmonized the underlying spatial schemas.

## Slide 3: Situation - ENC / DNC
The IHO Electronic Nautical Chart (ENC) and the Digital Nautical Chart (DNC) share the overall concept of producing an electronic product that can be used for navigation at sea
Both are typically derived from the conventional paper nautical chart in a vector form
ENC and DNC differ significantly - they are designed to operate in very different legal and operational environments and in conjunction with different suites of supporting data

## Slide 4: Background
Separate evolution of standards
Overlapping business requirements
Production inefficiencies
Operational responsiveness
Early harmonization efforts incomplete
Joint UK/US study on ‘Interoperability through Hydrographic Harmonization’ IDON 2003
Canada convened ad-hoc meeting of SMEs
Notes: <number>
<footer>
<header>
<date/time>
Military hydrographic community
  IHO S57 for ENC – Electronic Navigational Chart – serves both military and commercial
    Not global coverage
  DIGEST for DNC – Digital Nautical Chart – serves military only
    Global coverage
Production inefficiencies are magnified by separate update mechanisms required
Early Hydro harmonization work within DGIWG had many ad hoc mtgs, but never formally recognized, misplaced MOU between IHO and DGIWG

## Slide 5: Benefits
improvements in time/effort required to produce data
efficient database management (e.g., one update suitable for multiple products)
increased operational capability and system functionality (WECDIS user)
greater flexibility towards future enhancements and extensions
lower-cost COTS solutions; more vendor options
ease of maintenance of standards (e.g., S-57, DIGEST)
Notes: Confirm need to progress data interoperability issues
  Standards organizations (eg. IHO, DGIWG, NATO, ISO TC211) to take note of IDON Interoperability Study as a starting point
Propose reactivation of joint IHO/DGIWG Harmonization WG
  Initial period of 2 yrs
  Assumption of HIHWG
  Product to Product conversion was not viable
  Data conversion through a database is a cost effective solution
  Unlikely to get a 100% automated solution
  Manual intervention in a database, once only
  Manual intervention at product level, everytime

## Slide 6
HIHWG
An ad-hoc international effort
Participating nations – CAN, GBR, NZL, SWE, USA
Established to identify a solution to harmonise digital vector hydrographic data, focusing on ENC and DNC
Is a partnership between nations under the auspices of the DGIWG and the IHO
Notes: The Hydrographic Information Harmonisation Working Group (HIHWG) is an ad-hoc effort established to identify a solution to harmonize digital vector hydrographic data sets into a neutral database that can then be used to create subsequent products with consistency and without duplication of effort.
The HIHWG is a partnership between nations under the auspices of the DGIWG and the IHO.

## Slide 7
Contained as an annex to the DGIWG/IHO MoU
Formally defines structure, authority, membership, deliverables, timelines and success criteria
Required work is based on the recommendations from UK/US sponsored Interoperability Through Hydrographic Standards Harmonization: IDON, 2003
Terms of Reference (TOR)
Notes: HIHWG TOR is contained as an annex to the DGIWG/IHO MoU
The TOR formally defines structure, authority, membership, deliverables, timelines and success criteria
The HIHWG work is based on the recommendations from UK/US sponsored (tendered contract) report entitled;
Interoperability Through Hydrographic Standards Harmonization: IDON, 2003.

## Slide 8: HIHWG
Is Not
Is
Creating or modifying any existing standards or products
Developing the database solution
Developing software or system
Developing a one-step product converter
Developing a product update mechanism
Developing product input or export tools
Designing a Common Content Model
Developing a migration plan
Recommending a database approach
Concentrating on vector hydrographic information only
Influencing harmonisation of standards
Providing foundation for future interoperability
Developing XML Schemas
Notes: This is to reiterate what the HIHWG is and is not
What we are to deliver

## Slide 9: Objectives
Preserve the maximum amount of data content
Maintain the update functionality and providing for the production according to both product specifications
Promote interoperability
  Provide foundation for consistent products in multiple formats
  Increase the amount of source data that may be utilized to populate hydrographic data repositories
  Communicate implementation recommendations
Ensure future standards benefit from documented differences and the best practices/processes for the next generation products
Notes: Produce a set of resources and recommendations to assist in the harmonization and interoperability of digital hydrographic data.
Promote the implementation of this work for the benefit of safety and maritime navigation.
Deliver to key stakeholders a proposed communication plan to ensure the successful implementation of HIHWGs recommend database solution.
    Communicate the potential value the outcomes of this project holds for all stakeholders.
    Generate a common understanding of how this effort will improve the hydrographic products by promoting consistency of both content and accuracy.
    Prevent misconceptions and manage assumptions with respect to the conclusions of this work.
    Promote interoperability with current and future product usage.

## Slide 10: Potential Benefits (if implemented)
Reduced time and effort to produce data ($$$)
Efficiencies in database management ($)
Increased operational capability
Greater flexibility in support of future developments
Increased vendor options through SCOTS
Multiple hydro vector products from one database ($$)
Updates in multiple formats from a single source
Notes: Improvements in time & effort required to produce data - estimated at $3M/yr
Efficient database management (e.g., a single database generating multiple products)
Increased operational capability and system functionality (dual fuel for WECDIS users)
Greater flexibility towards future enhancements and extensions
Lower-cost Standards base Computer Off the Shelf (SCOTS) solutions; more vendor options
Multiple hydro vector products in a product neutral content model, following data input rules thereby providing consistent information and efficient database management (e.g. one update suitable for multiple products)

## Slide 11: Benefits to the Navy
Faster turn around on source data
  Digital data capture will require less time
  Better response to react to changing regional Op priorities
As the community moves to more modern data delivery mechanisms, the data will be ready to move forward to support more demanding data requirements (eg. Littoral operations)
Ability to support Mission Specific Data (MSD) requirements for mission planning and more agile customers of navigation data

## Slide 12: Approach
Creation of a Common Content Model (CCM) to hold and manage the superset of semantic concepts contained in both ENC and DNC
XML import rules to populate the CCM from ENC & DNC
XML export rules to extract features from the CCM to create ENC and DNC
  Feature content only
Potential to populate from and export to other products
Potential to extend or amend the CCM content
HIHWG Metadata Profile of ISO 19115:2003
Notes: The approach taken by HIHWG was the creation of a Common Content Model (CCM), which is essentially the description (in spreadsheet form) of a model for a product-neutral feature and metadata database. This CCM includes a set of import rules that enable the extraction of feature content and metadata from ENC and DNC products, to populate its’ predefined fields. The CCM also contains export rules to extract the data required from the CCM to create ENC and DNC products.
A CCM-based database could be populated from other sources and used to generate other products but the necessary import & export rules would need to be defined. Additionally, users could amend the CCM as required for new features, updated metadata etc.
This is illustrated in the following slide(s)

## Slide 13
Consistent
Feature & Attribute Mapping
Metadata
Geometry & Precision
HIHWG
Product
Neutral
Content Model
135
Other
Data Input Rules
Data Output Rules
ENC
Product
Spec
DNC
Product
Spec
135
Other
Product
Spec
DNC
ENC
HIHWG
Rules
Rules
Expandability
Notes: in order to harmonize, multiple hydro vector products are ingested into a HIH product-neutral content model following data input rules:
Concept of HIH Product Neutral Content Model/database
  Vector hydro products can be ingested using the data input rules
  Hydro information is stored as information and not as a product, a model of the real world object
  Maintenance of hydro information in a single database facilitates data consistency, and has potential to reduce manpower
  Data output rules are based on the product specifications that enable the generation of many consistent hydro products in the desired product format
A CCM-based database could be populated from other sources and used to generate other products but the necessary import & export rules would need to be defined. Additionally, users could amend the CCM as required for new features, updated metadata etc.

## Slide 14
Direct translation from ENC to DNC is not feasible, as suggested in the IDON report
Proposed
  that ingesting the data into a common data model is the most efficient way to manage data that supports both products.
Common Model
Benefit of requiring that each feature be maintained only once.
This common model displayed in the center is the union of both product models.
Allows for the preservation of a value or attribute that may not exist in one of the products
Minimizes data loss that would happen if direct translation were attempted.
Common Content Model

## Slide 15
Common Content Model (CCM) -Complex

## Slide 16: LATERAL BUOY
IF Non Conspicuous <> REF
CONRAD
Conspicuous
Non Conspicuous
Conspicuous
(Has Reflector)
ENC
REF
Reflector
No Reflector
DNC
Notes: Lateral buoy with
CONRAD – conspicuous to radar
Attaching a radar reflector to an otherwise, inconspicuous to radar, object is a method of making the object radar conspicuous
Logic is:
DNC
  If the object has a reflector, then it maps to both is ‘conspicuous’ and ‘has reflector’
  If no reflector, then there is no mapping to ENC
  ENC
  If conspicuous, the object may or may not have reflector so there is no direct mapping to DNC
  If non-conspicuous, the object cannot possibly have a reflector
  If it is known to have a reflector there is a direct map to DNC “Reflector”

## Slide 17
DNC – Retain area and point geometry Parse text for ENC sector angle values Extract nominal range for ENC
ENC - Retain point geometry Construct DNC® area geometry from ENC point geometry, nominal range and sector angle values
Geometry Issues
Light Sectors
Import
Notes: DNC doesn’t support co-incident geometry.
ENC reuses geometry ‘skin of the earth’ – consistent topology
DNC splits data into coverages to overcome this but inconsistencies exist between coverages and collapsing coverages often creates sliver polygons (controlling the collapse is necessary)
  In DNC, extra lines are required to close polygons due to DNC tiling
LIGHT SECTORS
The DNC cartographic object for light sectors can be constructed from the information derived from ENC but light and sector origin cannot be co-incident in DNC. Both positions can be imported or automate reference to another resource (eg.light list) on import
The ENC model for light sectors requires some manual intervention in order to derive the sector angle values from the DNC cartographic object.
The process now ensures that the appropriate information is captured within the database so that either product can be generated.
It is important to note that these processes to overcome issues are not always 100% automatic, we found that a number of problems required a semi-manual process. The group has outlined and described the type of production tool that would be required to support these semi-manual processes.
This is an example of some aspects of the Geometry work of the group.
The first three columns show some of the detail provided by the IDON report.
Each element identified by the report was looked at by the group to ensure that the issue was represented clearly and completely.
Under the context of a database solution and focusing on the steps required to import and export the products into the database. A process was identified for each issue outlined by the IDON report.
Using 3.14 Sector lights as an example we see how the DNC and ENC differ in the way they represent and capture the information.
The issue here is the mapping of the attribution on a point feature with a cartographic area feature.
The process developed by the group to over come the problem for sector light is captured here.

## Slide 18: HIHWG Metadata
Created DNC-ENC-AML vs. ISO metadata crosswalk
Identified core elements as well as commonalities between datasets
Identified no-matches (DNC)
Identified elements necessary to pass validation
Provided examples to HIHWG
Compiled Hydro Metadata Profile
Presented profile to IHO TSMAD in 2005
Notes: <number>
<footer>
<header>
<date/time>
Using the tables inherent in the hydro datasets, the metadata project team created a superset crosswalk against ISO 19115 Metadata.
This crosswalk was used to compile the hydro metadata profile of ISO 19115.
The PT has discovered the commonalities and deficiencies (mostly DNC) between the metadata carried in the datasets as well as the metadata which will be necessary to pass validation.
The next step will be to seek approval from IHO/TSMAD and DGIWG.
Once comments are received and necessary changes made, the PT will begin the first draft of the XML implementation of the profile.

## Slide 19: Recommendation - Future Harmonisation
Decisive action required to implement national solutions to exploit the HIHWG work
National ENC / DNC production will need to ensure that their national production systems are compatible with the HIHWG feature-attribute schemas to reap the significant benefits in exploitation of ENC / DNC data as source for their own national databases
  Ease of maintenance and updates
  Consistent data
  Improved ENC / DNC output

## Slide 20: NATO Activities
NATO Geospatial Maritime Working Group
Participating nations – CAN, DEN, EST, FRA, GBR, GER, GRE, ITA, NLD, NOR, POL, POR, SWE, TUR, USA
Focus is on REP (Recognized Environmental Picture) and AML STANAG
AML STANAG currently has 6 approved layers, additional 3 under development
  Examples:
    Routes, areas and limits
    Environment seabed and beach
    Contour line bathymetry